## Slide 1: Team Ink3D SRS Gate Review
Daniel Lain
Tim Edmonson
Shawn Simonson
Jesse Bowles

## Slide 2: Product Concept
Product: 3-D Printer Fabrication System
Problem Solved: The need to fabricate custom human compatible medical devices
Audience:
  Dr. Panos S. Shiakolas, Manufacturing Automation and Robotic Systems (MARS) lab at University of Texas Arlington,
  Medical Researchers
  Material Researchers

## Slide 3: Product Concept

## Slide 4: Functional Requirements
3.1 STL File Input
  3.1.1 Description: The system shall provide a way for the user to select an STL file and then input that STL file into the system for processing.
  3.1.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.1.3 Constraints: The system must support multi-material objects but the STL file format does not support material information.
  3.1.4 Standards: STL (STereo Lithography) File Format
  3.1.5 Priority: 1 – Critical
3.4 Issue Machine Instructions
  3.4.1 Description: The system shall issue generated machine instructions from the software component to the printing hardware component.
  3.4.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.4.3 Constraints: None
  3.4.4 Standards: GCode
  3.4.5 Priority: 1 – Critical

## Slide 5: Functional Requirements
3.5 Monitor Temperature
  3.5.1 Description: The system shall monitor input from heat sensors attached to the printing hardware. The temperature of each extruder’s nozzle must be monitored at all times to ensure that material is extruded at the proper temperature.
  3.5.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.5.3 Constraints: In order to monitor the temperature of different extruder nozzles, the printing hardware must output information describing the temperature of each extruder nozzle.
  3.5.4 Standards: None
  3.5.5 Priority: 1 – Critical
3.6 Monitor Position
  3.6.1 Description: The system shall monitor the position of the printing head at all times during operation. The system must be aware of the position of the printing head in order to adhere to a predefined printing path.
  3.6.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.6.3 Constraints: In order for the printing head position to be monitored by the system, the printing hardware must output information describing the position of the printing head.
  3.6.4 Standards: None
  3.6.5 Priority: 1 – Critical

## Slide 6: Functional Requirements
3.8 Identify Materials
  3.8.1 Description: The system shall identify every type of material that is being used for printing the 3D object.
  3.8.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.8.3 Constraints: None
  3.8.4 Standards: STL
  3.8.5 Priority: 1 - Critical
3.9 Identify Shapes
  3.9.1 Description: The system shall identify the shape of the object being printed by dividing it into smaller shapes for each individual material used.
  3.9.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.9.3 Constraints: Unification of multiple shapes within the same dimensional space.
  3.9.4 Standards: STL file
  3.9.5 Priority: 1 - Critical

## Slide 7: Functional Requirements
3.10 Determine Shape of Support Material Structure
  3.10.1 Description: The system shall determine the shape that the support material needs to be for stabilizing the 3D object as it is being printed. Without the support, the object could collapse during printing.
  3.10.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.10.3 Constraints: Complex analytical geometry.
  3.10.4 Standards: None
  3.10.5 Priority: 1 - Critical
3.11 Create Printing Path
  3.11.1 Description: The system shall determine a route that the printing head must follow as it prints.
  3.11.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.11.3 Constraints: Cannot print two materials on the same path.
  3.11.4 Standards: G-Code
  3.11.5 Priority: 1 - Critical

## Slide 8: Functional Requirements
3.14 Slice Geometry into Thickness Levels
  3.14.1 Description: The system shall be able to process geometry in such a way as to generate sub-models of appropriate and customizable thickness such that the 3D printer can print each layer of the given thickness.
  3.14.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.14.3 Constraints: None
  3.14.4 Standards: None
  3.14.5 Priority: 1 – Critical
3.17 Allow for UV Head Polymerization
  3.17.1 Description: The head shall be able to use UV light to cure or dry the extruded material. The system shall accommodate the use of UV to be turned on and off such that the material can be cured.
  3.17.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.17.3 Constraints: The system shall allow for duplicate paths.
  3.17.4 Standards: None
  3.17.5 Priority: 1 – Critical

## Slide 9: Functional Requirements
Non Critical Requirements
  3.16 Monitor Door Switch
  3.18 Sparsity and Density Controls

## Slide 10: User Interfaces Requirements
3.2 Graphical User Interface
  3.2.1 Description: The system shall provide a graphical user interface from which the user can import 3D models and initiate print operations. The GUI must be both intuitive and responsive.
  3.2.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.2.3 Constraints: None
  3.2.4 Standards: Java Swing/AWT
  3.2.5 Priority: 3 – Moderate
3.12 Database Interface
  3.12.1 Description: The system shall have an interface that allows the user to view what material is already stored in the database and enter new information for material not already stored.
  3.12.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.12.3 Constraints: None
  3.12.4 Standards: Java / Swing / AWT
  3.12.5 Priority: 1 - Critical

## Slide 11: User Interfaces Requirements
3.13 Store & Load Material Records
  3.13.1 Description: The system shall be able to load the material records stored in the materials database in order to control the temperature, movement speed, and flow speed of the nozzle at the correct setting.
  3.13.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.13.3 Constraints: None
  3.13.4 Standards: Must be able to be serialized.
  3.13.5 Priority: 1 – Critical
3.19 Graphical Object Models
  3.19.1 Description: The system shall display a graphical model of the objects represented by imported STL files. The user will be able to drag the graphical model around on a virtual printer bed in order to specify the location on the printer bed where the object will be printed.
  3.19.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  3.19.3 Constraints: This will require graphics processing and may make the GUI unresponsive.
  3.19.4 Standards: None
  3.19.5 Priority: 5 – Future

## Slide 12: User Interface

## Slide 13: Inputs and Outputs
Inputs
  STL File
  Material Data
  GUI Selection
  Start Printing
  Stop/Pause Printing
  Heat Sensor
  Position Sensor
  Flow Sensor
  Door Sensor
Outputs
  G-Codes
  State Notification
  Confirmation Message(s)
  Printed Object

## Slide 14: Packaging Requirements
4.1 Software Installer
  4.1.1 Description: The host software shall be delivered as an executable installer via USB flash memory and Compact Disc.
  4.1.2 Source: Dan Lain (Team Member)
  4.1.3 Constraints: None
  4.1.4 Standards: Windows Installer
  4.1.5 Priority: 1 – Critical
4.2 Host Software to Printer Connection
  4.2.1 Description: The host software shall be connected to the printing hardware using a DE-9, DB-25, or Universal Serial Bus cable.
  4.2.2 Source: Shawn Simonson (Team Member)
  4.2.3 Constraints: None
  4.2.4 Standards: USB, RS-232
  4.2.5 Priority: 1 – Critical

## Slide 15: Packaging Requirements
4.3 User Manual
  4.3.1 Description: The system shall be delivered with a user manual. The user manual will include detailed instructions on how to operate the host software and how to properly connect the host software to the printer.
  4.3.2 Source: Tim Edmondson (Team Member)
  4.3.3 Constraints: None
  4.3.4 Standards: None
  4.3.5 Priority: 3 - Moderate

## Slide 16: Performance Requirements
5.1 Startup Time
  5.1.1 Description: The host software shall start in one minute or less.
  5.1.2 Source: Tim Edmondson (Team Member)
  5.1.3 Constraints: None
  5.1.4 Standards: None
  5.1.5 Priority: 4 – Low
5.2 STL Import Time
  5.2.1 Description: The host software shall import STL files in one minute or less.
  5.2.2 Source: Tim Edmondson (Team Member)
  5.2.3 Constraints: None
  5.2.4 Standards: The STL file format will be imported.
  5.2.5 Priority: 4 – Low

## Slide 17: Performance Requirements
5.3 Object Processing Time
  5.3.1 Description: The host software shall perform object processing and machine instruction generation in five minute or less.
  5.3.2 Source: Tim Edmondson (Team Member)
  5.3.3 Constraints: The geometric processing algorithms used to process objects must be efficient.
  5.3.4 Standards: None
  5.3.5 Priority: 2 – High
5.4 GUI Responsiveness
  5.4.1 Description: The graphical components of the user interface shall be responsive to user interaction.
  5.4.2 Source: Tim Edmondson (Team Member)
  5.4.3 Constraints: In order to achieve a responsive user interface, multi-thread processing may be required.
  5.4.4 Standards: None
  5.4.5 Priority: 3 – Moderate

## Slide 18: Performance Requirements
5.5 Real Time Sensor Monitoring
  5.5.1 Description: The system shall monitor data from sensors in real time during operation. The sensor data must be monitored in real time to ensure proper printer functionality as well as enforce safety systems.
  5.5.2 Source: Tim Edmondson (Team Member)
  5.5.3 Constraints: Constant monitoring of sensors could require expensive processing and memory resources.
  5.5.4 Standards: None
  5.5.5 Priority: 2 – High

## Slide 19: Other Requirements : Safety
6.1 Temperature Cutoff Threshold
  6.1.1 Description: The system shall include a temperature cutoff threshold for the printer head. If the temperature of the printer head reaches the cutoff temperature, the system will abort the operation and shut off the heating device.
  6.1.2 Source: Tim Edmondson (Team Member)
  6.1.3 Constraints: The system must be able to accurately monitor the temperature of each printing head.
  6.1.4 Standards: None
  6.1.5 Priority: 1 – Critical
6.2 Printing Area Restrictions
  6.2.1 Description: The system shall only extrude material within a configured area. Material extruded by the printer will be at a high temperature and may cause harm to the printer’s surroundings; therefore it is important to ensure that the material is only extruded in a specified safe area.
  6.2.2 Source: Tim Edmondson (Team Member)
  6.2.3 Constraints: None
  6.2.4 Standards: None
  6.2.5 Priority: 1 – Critical

## Slide 20: Other Requirements: Maintenance and Support
7.1 Host Software Manual
  7.1.1 Description: A manual that details the operation of the host software shall be provided. Here, “host software” is that software which is run on the workstation that generates machine instructions for the printing hardware. The manual must detail common troubleshooting issues as well as provide basic usage instructions.
  7.1.2 Source: Shawn Simonson (Team Member)
  7.1.3 Constraints: None
  7.1.4 Standards: None
  7.1.5 Priority: 1 – Critical
7.2 Source Code Documentation
  7.2.1 Description: The source code developed by the software team shall be well documented with comments explaining the functionality of all modules and any non- obvious code. This documentation is intended to support any future development on the system.
  7.2.2 Source: Tim Edmondson (Team Member)
  7.2.3 Constraints: None
  7.2.4 Standards: None
  7.2.5 Priority: 2 – High

## Slide 21: Other Requirements: Maintenance and Support
7.3 Source Code Availability
  7.3.1 Description: The source code developed by the software team shall be freely available to developers and the public. The source code will be hosted on a public repository.
  7.3.2 Source: Shawn Simonson (Team Members)
  7.3.3 Constraints: None
  7.3.4 Standards: Git, SVN
  7.3.5 Priority: 2 – High

## Slide 22: Other Requirements: Additional
8.1 Material Database
  8.1.1 Description: The system shall have a database that holds information about how the material is printed. For each material, the database must hold the diameter of the material filament and the temperature the filament must be extruded at.
  8.1.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  8.1.3 Constraints: None
  8.1.4 Standards: Binary Text
  8.1.5 Priority: 1 – Critical
8.2 Abstract Hardware Interface
  8.2.1 Description: The system shall allow for multiple different printers and multiple different heads to be used with minimal software change.
  8.2.2 Source: Jesse Bowles (Team Member)
  8.2.3 Constraints: Unknown hardware interface
  8.2.4 Standards: None
  8.2.5 Priority: 1 – Critical

## Slide 23: Other Requirements: Additional
8.3 Modular and Scalable Design
  8.3.1 Description: The software shall be developed using proven design principles to ensure that it can be scaled and maintained by future development teams.
  8.3.2 Source: Dr. Panos S. Shiakolas (Sponsor)
  8.3.3 Constraints: None
  8.3.4 Standards: S.O.L.I.D. Design Principles
  8.3.5 Priority: 1 – Critical

## Slide 24: Other Requirements: Acceptance Criteria
9.1 Verify that the system reads STL files
  9.1.1 Requirement(s) addressed:
    3.1 – STL File Input
  9.1.2 Verification Procedure: The user will be able to see the file has been accepted and the file name will be displayed in the GUI.
9.2 Verify the database interface
  9.2.1 Requirement(s) addressed:
      3.2 – Graphical User Interface
      3.13 – Database Interface
      3.14 – Store and Load Material Records
      8.1 – Material Database
  9.2.2 Verification Procedure: The user will load the GUI and click on the view/edit database button. The user then will see and be able to edit stored values. Upon changing values the user will return to the main menu. Clicking on the view/edit button again will display the edited values.

## Slide 25: Other Requirements: Acceptance Criteria
9.3 Verify the system prints a model
  9.3.1 Requirement(s) addressed:
    3.1 – STL File Input 3.3 – Generate Machine Instructions
    3.4 – Issue Machine Instructions 3.6 – Monitor Temperature
    3.7 – Monitor Position 3.8 – Identify Material Constraints
    3.9 – Identify Materials 3.10 – Identify Shapes
    3.11 – Determine Shape of Support Material Structure 3.12 – Create Printing Path
    3.14 – Store and Load Material Records 3.15 – Slice Geometry into Thickness Levels
    3.16 – Monitor Flow Sensors 4.2 – Host Software to Printer Connection
  9.3.2 Verification Procedure: The user will load an STL file and click print. The system will then print the correct shape and material.
9.4 Verify the system stops printing of out of operational range
  9.4.1 Requirement(s) addressed:
    6.1 – Temperature cutoff threshold 3.16 – Monitor Flow Sensors
  9.4.2 Verification Procedure: During a print run a fan will be pointed at the head reducing its temperature to below specified material requirements and the printer will stop printing until the temperature is raised to the correct level.

## Slide 26: Use Case Diagram

## Slide 27: Use Cases
10.1 Import STL File to System
10.1.1 Scenario: The user selects an STL file to be printed.
10.1.2 Actor(s): The user
10.1.3 TUCBW: The user clicks the “Import STL” button
10.1.4 TUCEW: The user sees the confirmation message that STL file was successfully uploaded.
10.2 Print 3D Object
10.2.1 Scenario: The user uses the system to print an STL file as a physical 3D object.
10.2.2 Actor(s): The user
10.2.3 TUCBW: The user clicks the print button.
10.2.4 TUCEW: The user sees the physical 3D object on the platform.
10.3 Edit Material Database
10.3.1 Scenario: The user can add new or modify material information in the database.
10.3.2 Actor(s): The user
10.3.3 TUCBW: The user clicks the “Update Materials” button.
10.3.4 TUCEW: The user sees the material updated in the database.