## Slide 1: Team Ink3D Architecture Design Specification Review
Daniel Lain
Tim Edmonson
Shawn Simonson
Jesse Bowles

## Slide 2: Outline
Vision
Guiding Principles
Layer Overview
Detailed Layer Subsystem Descriptions

## Slide 3: Architectural Vision
Software system for unknown hardware implementation
Multiple materials
Evolution of Hardware and Software
Guiding Principles
  Modularity
  Configurability
  Extensibility
  Portability

## Slide 4: Guiding Principle
Modularity
  Layer replacement
  Loose coupling
Design implications
  Interfaces defined
  High cohesion
  Unidirectional data flows
  Abstraction

## Slide 5: Guiding Principle
Configurability
  Printer Configurability
  Print Configurability
  Material Configurability
Design implications
  Package interfaces
  Configuration pass through
  Concrete implementation selection

## Slide 6: Guiding Principle
Extensibility
  Reusable sub-systems
  Need to add future sub-systems
  Maintainable codebase
Design implications
  Abstract interfaces
  Composite configurations
  Establish frameworks

## Slide 7: Layer Structure

## Slide 8: User Interface Layer
Interface to user
  Import Files
  Configure Materials
  Configure Printer
  Initiate Print
  Pause / Resume
  Printer Status
Packages Print Data for Preprocessing
Expectations
  User Input
  Printer feedback

## Slide 9: Preprocessing Layer
Interface to processing layer
  Translates data format
Re-Packages Print Data for Processing
Expectations
  Standard format object file
  Configuration data

## Slide 10: Processing Layer
Slice and generate G-Code
  Translates object file to path
Packages G-Code and Configuration
Expectations
  Normalized object data
  Configuration data

## Slide 11: Post-Processing Layer
G-Code Preparation
  Prepare G-Code based on configuration
Re-Packages G-Code and Configuration
Expectations
  Standard G-Code path
  Configuration data

## Slide 12: Physical Layer
Printer Interface
  Printer state control
  Packet preparation
Provides
  Pause / Resume
  Instruction stream
Expectations
  Printer specific G-Code path
  Configuration data

## Slide 13: Printer Feedback Layer
Printer monitoring
  Status collection
Provides
  Status Notification
  State Change Notification
Expectations
  Printer Status

## Slide 14: Layer Subsystem Overview

## Slide 15: User Interface Layer Subsystems

## Slide 16: User Interface Layer Subsystems
Import Module
  Purpose: Allow the user to import object files
  Function: Display interface from which users import files and pass those files to the Print Module.
  Dependencies: Print Module
  Processing: Create reference to an object file.
  Input: Object File Name
  Output: Object File Reference

## Slide 17: User Interface Layer Subsystems
Print Module
  Purpose: Allow user to set print specific settings and initiate a print job.
  Function: Display interface from which users can set print settings and initiate a print. Pass the necessary information to the Preprocessing Layer when a print is initiated.
  Dependencies: Database Interface
  Processing: Map materials to object files. Package print request object.
  Input: Print Settings, Printer Configuration, Material Data, Object File References
  Output: Print Packet (Encapsulates Print Settings, Printer Configuration, Material Data, Object File References)

## Slide 18: User Interface Layer Subsystems
Configuration Module
  Purpose: Allow the user to configure printer settings and material information.
  Function: Display interface from which users can input printer configuration and material information. Pass information to the Database Interface to be saved.
  Dependencies: Database Interface
  Processing: User Input Processing
  Input: Printer Configuration Data, Material Data
  Output: Printer Configuration Data, Material Data

## Slide 19: User Interface Layer Subsystems
Database Interface
  Purpose: Abstract data persistence
  Function: Receive data from other modules and store it in a database. Retrieve data from the database for other modules.
  Dependencies: None
  Processing: Database query generation
  Input: Configuration Information
  Output: CRUD Operations, Configuration Information

## Slide 20: User Interface Layer Subsystems
Status Module
  Purpose: Display printer status information to the user and allow the user to stop/pause/resume a print job.
  Function: Interpret data from the Printer Feedback Layer and display the data to the user. Send stop/pause/resume commands to the Physical Layer.
  Processing: User Input Processing
  Input: Stop/Pause/Resume User Input, Printer State Data, Configuration Data
  Output: Stop/Pause/Resume Command

## Slide 21: Preprocessing Layer Subsystems

## Slide 22: Preprocessing Layer Subsystems
Normalization Module
  Purpose: Provide a uniform interface between the Print Module and the Processing Layer.
  Function: Translate and repackage the print request object in to the format that the processing layer needs
  Dependencies: Print Module
  Processing: Normalizes Object File
  Input: Packet of Files
    The Object(s)
    Material(s)
    Printer Configuration
  Output: Packet of Files
    Normalized Object
    Definition
    Print Configuration

## Slide 23: Processing Layer Subsystems

## Slide 24: Processing Layer Subsystems
Slicing Engine
  Purpose: Create a set of instructions for the print job
  Function: Uses the Object File to create a printing path.
  Dependencies: Normalization Module
  Processing: Slices object into layers
  Input: Packet of Files
    Normalized Object
    Definition
    Print Configuration
  Output: Packet of Files
    G-Code
    Print Configuration

## Slide 25: Post Processing Layer Subsystems

## Slide 26: Post Processing Layer Subsystems
G-Code Preparation
  Purpose: To modify the instructions for the printer to accept.
  Function: Adds instructions for unique commands for the particular printer
  Dependencies: Slicing Engine
  Processing: Modifies G-Code
  Input: Packet of Files
    G-Code
    Print Configuration
  Output: Packet of Files
    G-Code
    Print Configuration

## Slide 27: Physical Layer Subsystems

## Slide 28: Physical Layer Subsystems
Printer State Controller
  Purpose: To conditionally dispatch G-Codes to packet preparation module based on printer and operator state.
  Function: Accept status inputs from status module and printer state monitoring and conditionally dispatches G-Code stream to packet preparation module.
  Dependencies: Packet preparation module, status module, and printer state monitoring module.
  Processing: May insert G-codes to halt the print if necessary.
  Input: Error State, Packet of Files
    G-Code
    Print Configuration
  Output: G-Code

## Slide 29: Physical Layer Subsystems
Packet Preparation
  Purpose: Convert G-Code stream into byte-stream for printer.
  Function: Serialize G-Code stream and packetize so that the packets can be transmitted to the printer. Establish serial connection to printer firmware.
  Dependencies: Printer state controller.
  Processing: Serialization of G-Code stream. Chunk serialized G-Code stream into packets to be sent to printer firmware.
  Input: G-Code
  Output: Bits on a Wire

## Slide 30: Printer Feedback Layer Subsystems

## Slide 31: Printer Feedback Layer Subsystems
State Monitoring
  Purpose: To monitor the operating status of the printer hardware.
  Function: Listens for response from printer on established serial connection. Assembles and converts received data into form appropriate for inter-layer transmission.
  Dependencies: Printer State Controller, Status Module
  Processing: Data conversion from printer byte-stream into data structure suitable for transmission to other layers in the system.
  Input: State Info
  Output: Error State, State Info