## Slide 1: Printer State Controller – Unit Tests
PS1 and PS3 ensure that G-Code stream is correctly acted upon in response to user input.
Outbound G-Codes will be written to log and compared against incoming G-Codes.
When the user cancels or pause/resumes print job in the UI menu, the PSC (Printer State Controller) will perform an action. This action will be reflected in the outbound G-Codes which can be compared to the inbound G-Codes for correctness.
PS1 | G-Codes User Interface Status (Cancel) | The Printer State Controller shall halt the sending of G-Codes to the Serialization Module. | Manually build PrintJobConfiguration object with test G-Codes. Trigger cancel event to ensure that no further G-Codes are sent to Serialization Module. There is no return state. Therefore, the print job cannot be resumed.
PS3 | G-Codes and User Interface Status (Pause/Resume) | The Printer State Controller shall halt the sending of G-Codes to the Serialization Module until resume action is received. | Manually build PrintJobConfiguration object with test G-Codes. Trigger pause event to ensure that no further G-Codes are sent to Serialization Module. Trigger resume event to ensure that G-Codes resume transmission from prior state.

## Slide 2: Printer State Controller – Unit Tests (cont.)
PS2 | G-Codes Printer Feedback Status (Temperature and Position) | The Printer State Controller shall consume temperature and position information from Printer Feedback Status and insert halt command into the G-Code buffer to stop the print when values are out of range. | Manually build PrintJobConfiguration object with test G-Codes. Manually build Printer State Object with out-of-bounds operating parameters. Ensure that proper halt G-Codes are inserted into the output G-Code buffer.
PS2 ensures that the G-Code stream is correctly acted upon in response to printer feedback (temperature, arm position)
Verified in the same manner that PS1 and PS3 are verified.
The exception is that the action is based on printer feedback and not user input.

## Slide 3: Dispatch Module – Unit Tests
DM1 | De-Serialized printer feedback information | Populated PrinterFeedback object | Build de-serialized printer feedback object which represents the de-serialized printer feedback data. Verify that the PrinterFeedback Object is built correctly by the Dispatch Module.
Manual test involves building test printer feedback data.
We will feed mock positions and temperatures to dispatch module
To Verify, we check that the PrinterFeedback Object is correctly built by displaying or logging the contents of the PrinterFeedback Object

## Slide 4: Serialization Module – Unit Test
SE1 | Finalized G-Codes | Serialized stream of G-Codes to be sent to the printer | Manually build simple G-Code set to be tested. Inspect and verify that Serialization Module serializes G-Codes without serialization errors.
The Serialization Module will be passed a test set of G-Codes
The Serialization Module will serialize the G-Codes and print the serialized results to a log
The log can be manually inspected for serialization errors (out of order or missing data for example).
Deserialization Module – Unit Test
DS1 | Serialized byte-stream of printer feedback information | De-Serialized printer feedback object | Build test program that establishes connection to the printer and issues simple G-Codes. Connect test PC to printer and monitor feedback stream from printer. Inspect and verify that the de-serialized printer feedback object is built correctly. Inspection and verification can be accomplished with a Java debugger hooked into the test program.
The Deserialization Module can be tested in real time.
Can set break condition in Java debugger such that we can step into the debugger when printer feedback has been assembled into a printer feedback object.
Will compare printer feedback object to printer feedback in debugger.

## Slide 5: Tx/Rx Module – Unit Tests
TR2 | Serialized G-Code stream | Successfully poll and lock printer G-Code buffer. Write serialized G-Code stream to printer firmware. | Using the test program that establishes a connection to the printer, we will poll the printer, lock the G-Code buffer and verify that the test G-Codes have been sent. This can be verified visually as the printer executes the commands and via the printer feedback stream.
TR3 | Byte-stream of printer feedback information from printer | Successfully populate printer feedback buffer and raise a “buffer ready” flag signifying that printer feedback data is ready. | Using the test program that establishes a connection to the printer, we will continually monitor the input stream for printer feedback. We will verify that the feedback data buffer has been populated, is recent, and raises the ready flag. This can be inspected and verified with a Java debugger hooked into the test program.
TR1 | PrintJobConfiguration object | Successfully establish connection to printer firmware via virtual serial communications using the parameters specified within the PrintJobConfiguration object. | Manually build a PrintJobConfiguration object with connection information. The test PrintJobConfiguration object will be passed to a small test program that uses its information to establish connection to the printer firmware.
Testing the Tx/Rx Module involves building a small test program.
The first task is to ensure that given a test PrintJobConfiguration Object, the module can establish a connection to the printer.
Requires physical printer to be tested.