## Slide 1: Team Ink3D Detail Design Specification Review
Daniel Lain
Tim Edmonson
Shawn Simonson
Jesse Bowles

## Slide 2: Outline
Architecture Overview
Module Overview
Critical Data Object Requirements
Detail Module Descriptions
Requirements Traceability
Acceptance Plan

## Slide 3: Architecture Overview
Configurability
Modularity
Expandability
Portability
Multiple Materials

## Slide 4: Architecture Design
Seven Layers
Layer Independence
Interface Based
Master Configuration Object

## Slide 5: Module Decomposition
High Cohesion
Low Coupling
Master Configuration Object

## Slide 6: Module Data Flows
Many GUI Exchanges
Very Little In Processing
Layer | Data Flow ID | Data
Outside Inputs | OI1 | Object file of the STL file to be printed
 | OI2 | Printer configuration data entry values
 | OI3 | Material configuration data entry values
 | OI4 | Print configuration data entry values
 | OI5 | Print selections and button press
 | OI6 | Pause, resume, and stop button Presses
 | OI7 | Disk reads of XML and Directory structure
 | OI8 | Printer state information
 | OI9 | OS Driver information
 | OI10 | Extruder configuration data entry values
User Interface Layer | UI1 | Import file name
 | UI2 | Success state of import
 | UI3 | Loaded printer configuration
 | UI4 | Save printer configuration request
 | UI5 | Save material configuration request
 | UI6 | Loaded material configuration
 | UI7 | Loaded print configuration
 | UI8 | Save print configuration request
 | UI9 | Loaded configuration data
 | UI10 | Run print job
 | UI11 | Pause, resume, and stop button Presses
 | UI12 | Printer state information
 | UI13 | File Configuration object
 | UI14 | Printer configuration object
 | UI15 | Material configuration object
 | UI16 | Print Configuration object
 | UI17 | All requested configuration objects
 | UI18 | Object save/load requests
 | UI19 | Object save/load results
 | UI20 | XML File writes to disk
 | UI21 | Save print job configuration
 | UI22 | Print package object
 | UI23 | Print, Pause, Resume request
 | UI24 | Loaded Extruder Configuration Data
 | UI25 | Save Extruder Configuration Request
 | UI26 | Extruder Configuration Object
Preprocessing Layer | PR1 | Print package object
 | PR2 | Print package object
Processing Layer | PO1 | Print package object
Post-Processing Layer | PP1 | Print package object
 | PP2 | Print package object
Printer Control Layer | PL1 | G-Code
Communications Layer | CL1 | Serialized G-Codes
 | CL2 | Serialized printer state
 | CL3 | Command stream
Printer Feedback Layer | PF1 | Printer State Object
 | PF2 | Printer State Object

## Slide 7: Producer Consumer Table
Many GUI Exchanges
Very Little In Processing

## Slide 8: Print Job Configuration Object

## Slide 9: Printer Configuration Object
Name | Data Type | Description | Units | Boundaries
bedX | double | The max x of the bed. | mm | Greater than 0.
bedY | double | The max y of the bed. | mm | Greater than 0.
printCenterX | double | The x of the center of the print. | mm | 0 – bedX
printCenterY | double | The y of the center of the print. | mm | 0 – bedY
zOffset | double | The zOffset of the print bed surfaces. Used if the bed does not sit exactly at z = 0. | mm | Greater than or equal to 0.
gCodeFlavor | String | The G-Code flavor to output. | N/A | Within the set of available G-Code flavors.
useRelativeEDistances | boolean | When true, uses relative E values (required by some firmwares). | N/A | True or false
numExtruders | int | The number of extruders on the printer. | N/A | Greater than 0.
vibrationLimit | double | The limit of vibrations (in Hz) where movements will be slowed. If a move hits the specified vibration frequency, the extruder will slow. | Hz | Greater than or equal to 0.
comPortDescriptor | String | The descriptor for the com port the printer is connected to. Used to establish a connection to the printer. | N/A | N/A
baudRate | int | The baud rate for the printer. | Pulses per second | 0 - 250000
forceACK | boolean | States whether or not to use ACK as part of the protocol when communicating with the printer. | N/A | True or false
positionOffsetX | ArrayList<Double> | The x offset to apply to the extruder positions for the printer. These offsets are stored in an ArrayList where index 0 represents the x offset for position 0, etc. | mm | Double precision floating point boundaries.
positionOffsetY | ArrayList<Double> | The y offset to apply to the extruder positions for the printer. These offsets are stored in an ArrayList where index 0 represents the y offset for position 0, etc. | mm | Double precision floating point boundaries.
positionOffsetZ | ArrayList<Double> | The z offset to apply to the extruder positions for the printer. These offsets are stored in an ArrayList where index 0 represents the z offset for position 0, etc. | mm | Double precision floating point boundaries.
customStartGCode | String | The custom G-Code to run when the printer starts. | N/A | G-Codes that are understood by the printer.
customEndGCode | String | The custom G-Code to run when the printer shuts down. | N/A | G-Codes that are understood by the printer.

## Slide 10: Printer Status Object
Name | Data Type | Description | Units | Boundaries
extruderTemperature | ArrayList<Double> | An ArrayList containing the current temperature of each extruder. | degrees C | Set by the material constraints of the materials in each extruder.
bedTemperature | double | The current temperature of the printer bed. | degrees C | Set by the printer configuration constraints.
positionX | double | The x position of the first extruder. | mm | Set by the printer configuration contraints.
positionY | double | The y position of the first extruder. | mm | Set by the printer configuration contraints.
positionZ | double | The z position of the first extruder. | mm | Set by the printer configuration contraints.
gCodesExectured | List <String> | The last 5 GCodes executed. | N/A | N/A

## Slide 11: Subsection Configuration Object
Name | Data Type | Description | Units | Boundaries
bottomZ | double | The bottom of the subsection with relation to the entire object to be printed. | mm | Greater or equal to 0.
topZ | double | The top of the subsection with relation to the entire object to be printed. | mm | Greater than 0 and less than the total height of the object.
amfFile | File | The reference to the AMF file of the subsection. This is set during preprocessing. | N/A | N/A
gCodeFile | File | The reference to the gCode file of the subsection. This is set during processing. | N/A | N/A

## Slide 12: Print Configuration Object
Name | Data Type | Description | Units | Boundaries
customStartGCode | String | The custom G-Code to run when the print starts. | N/A | G-Codes that are understood by the printer.
customEndGCode | String | The custom G-Code to run when the print ends. | N/A | G-Codes that are understood by the printer.

## Slide 13: Infill Configuration Object
Name | Data Type | Description | Units | Boundaries
infillDensity | double | The density of infill from 0.0 - 1.0. 0.0 being no infill, 1.0 being a solid infill. | Ratio | 0.0 – 1.0
infillPattern | String | The pattern to use for internal infill. | N/A | Within set of available infill patterns.
topBottomInfillPattern | String | The pattern to use for the top and bottom layers' infill. | N/A | Within set of available infill patterns.
infillEveryNLayers | int | The ratio of layers to infill layers expresses as an integer >= 1. For example, infillEveryNLayers = 2 results in using infill every other layer, while infillEveryNLayers = 1 results in infill every layer. | N/A | Greater than or equal to 1.
onlyInfillWhereNeeded | boolean | When set to true, infill is treated as support material and only extruded where necessary. | N/A | True or false
solidInfillEveryNLayers | int | When set to a integer other than 0, a layer of solid infill with be extruded n layers, where the value of solidInfillEveryNLayers is n. | N/A | Greater than or equal to 0.
infillAngle | int | Default base angle for fill orientation in degrees from 0 to 359. This is the angle the infill will oriented in relation to the vertical perimeters. | degrees | 0 – 359
solidInfillThresholdArea | int | The threshold for area in square mm for which to force solid infill. | mm2 | Greater or equal to 0.
onlyRetractInfillWhenCrossingPerimeters | boolean | When set to true, filament will not be retracted unless crossing a perimeter, resulting in some visible oozing throughout the infill. | N/A | True or false
infillBeforePerimeters | boolean | When set to true, infill for each layer will be extruded before the perimeters are extruded. | N/A | True or false

## Slide 14: Layer & Perimeter Configuration Object
Name | Data Type | Description | Units | Boundaries
layerHeight | double | The height of each layer in mm. | mm | Greater than 0.
firstLayerHeight | double | The height of the first layer of the print in mm. | mm | Greater than 0.
perimeters | int | The number of vertical perimeters in the print. Essentially the number of "walls" around the perimeter of the print. | N/A | Greater than or equal to 0.
randomizedStartingPoints | boolean | If true, each layer should start from a different vertex to avoid build up on a specific corner. | N/A | True or false
generateExtraPerimetersWhenNeeded | boolean | If true, extra perimeters should be added in slopes where more than the specified number of perimeters is needed. | N/A | True or false
solidTopLayers | int | The number of solid layers to generate on the top of the print. | Layers | Greater than or equal to 0.
solidBottomLayers | int | The number of solid layers to generate on the bottom of the print. | Layers | Greater than or equal to 0.

## Slide 15: Speed Configuration Object
Name | Data Type | Description | Units | Boundaries
perimetersSpeed | double | Speed for perimeters | mm/s | Greater than 0.
smallPerimetersSpeed | double | Speed for small perimeters | mm/s | Greater than 0.
externalPerimetersSpeed | double | Speed for external perimeters | mm/s | Greater than 0.
infillSpeed | double | Speed for infill | mm/s | Greater than 0.
solidInfillSpeed | double | Speed for solid infill | mm/s | Greater than 0.
topSolidInfillSpeed | double | Speed for top solid infill | mm/s | Greater than 0.
supportMaterialSpeed | double | Speed for support material | mm/s | Greater than 0.
bridgesSpeed | double | Speed for bridges | mm/s | Greater than 0.
gapFillSpeed | double | Speed for gap fill | mm/s | Greater than 0.
nonPrintMovesSpeed | double | Speed for non prdouble movements | mm/s | Greater than 0.
firstLayerSpeed | double | Speed for the first layer | mm/s | Greater than 0.
perimetersAcceleration | double | Acceleration for perimeters | mm/s2 | Greater than or equal to 0.
infillAcceleration | double | Acceleration for infill | mm/s2 | Greater than or equal to 0.
bridgeAcceleration | double | Acceleration for bridges | mm/s2 | Greater than or equal to 0.
defaultAcceleration | double | Default Acceleration | mm/s2 | Greater than or equal to 0.

## Slide 16: Skirt & Brim Configuration Object
Name | Data Type | Description | Units | Boundaries
skirtLoops | int | The number loops of skirt to extrude (0 will extrude no skirt). | Loops | Greater than or equal to 0.
skirtDistanceFromObject | double | The distance from the object the skirt will be extruded at in mm >= 0. Setting this to 0 will essentially turn the skirt into brim. | mm | Greater than or equal to 0.
skirtHeight | int | The height of the skirt in layers >= 1. | Layers | Greater than or equal to 1.
skirtMinimumExtrusionLength | double | The minimum extrusion length of the skirt in mm >= 0. | mm | Greater than or equal to 0.
brimWidth | double | The width of the brim in mm (0 will extrude no brim). | mm | Greater than or equal to 0.

## Slide 17: Support Material Configuration Object
Name | Data Type | Description | Units | Boundaries
generateSupportMaterial | boolean | When set to true, G-code for support material will be generated. | N/A | True or false
overhangThreshold | int | The overhang threshold in degrees. Support material will not be for overhangs whose slope angle is above this threshold. | degrees | 0 – 180
enforceSupportForFirstNLayers | int | Forces support material on the first n layers. | Layers | Greater than or equal to 0.
raftLayers | int | Number of raft layers to print below the object. | Layers | Greater than or equal to 0.
supportMaterialPattern | String | Pattern used to generate support material. | N/A | Within set of available infill patterns.
supportPatternSpacing | double | The spacing in mm between support lines. | mm | Greater than or equal to 0.
supportPatternAngle | int | The angle the support pattern is extruded at (between 0 and 359). | degrees | 0 – 359
interfaceLayers | int | The number of interface layers to print between the raft and object. | Layers | Greater than or equal to 0.
interfacePatternSpacing | double | The spacing in mm between support lines. | mm | Greater than or equal to 0.

## Slide 18: File Configuration Object
Name | Data Type | Description | Units | Boundaries
parentSTLFile | File | The reference to the parent STL that will be subsectioned in the preprocessing layer. | N/A | N/A
subsectionSTLFile | File | The reference to the STL file that represents the subsection of the parent STL file. This is set in the preprocessing layer. | N/A | N/A

## Slide 19: Material Configuration Object
Name | Data Type | Description | Units | Boundaries
filamentDiameter | double | Diameter in mm of the filament. | mm | Greater than 0.
extrusionMultiplier | double | Flow rate multiplier. This changes the flow rate proportionally. 0.9 will be 90% flow rate, while 1.1 will be 110% flow rate. | Ratio | Greater than 0.0.
firstLayerExtrusionTemperature | int | The temperature (in degrees C) the extruder needs to be to extrude the first layer of this material. | degrees C | Within extruder temperature range.
extrusionTemperature | int | The temperature (in degrees C) the extruder needs to be to extrude this material. | degrees C | Within extruder temperature range.
retractionLength | double | Length (in mm) to retract during retraction. 0 to disable retraction. | mm | Greater than or equal to 0.
retractionLiftZ | double | The (positive) z value to quickly lift the extruder by during a retraction. | mm | Greater than or equal to 0.
retractionSpeed | int | The speed (in mm/s) at which to retract the filament during retraction (extruder motor speed). | mm/s | Greater than or equal to 0.
extraLengthAfterRetraction | double | The extra length of filament to push out during the first extrude after a retraction. | mm | Greater than or equal to 0.
minimumTravelAfterRetraction | double | Retraction is not triggered when travel moves shorter than this distance. | mm | Greater than or equal to 0.
retractOnLayerChange | boolean | When set to true, retraction will be triggered on each layer change. | N/A | True or false
wipeBeforeRetract | boolean | When set to true, the nozzle will be moved while retracting to reduce blob. | N/A | True or false
retractionLengthBeforeToolChange | double | Length (in mm) to retract when the tool is disabled. | mm | Greater than or equal to 0.
extraLengthOnToolReenable | double | The extra length of filament to push out during the first extrude after the tool is re-enabled. | mm | Greater than or equal to 0.
fanAlwaysOn | boolean | When set to true, fan will always run at at least minimum speed. | N/A | True or false
enableAutoCooling | boolean | When set to true, fan speed will automatically be set based on printing time. | N/A | True or false
minFanSpeed | int | The minimum fan speed in PWM. | PWM | 0 – maxFanSpeed
maxFanSpeed | int | The maximum fan speed in PWM. | PWM | minFanSpeed – 100
bridgeFanSpeedPercent | int | The percentage of default fan speed used for bridges expressed as an int (100 = 100%) | % | 0 – 100
disableFanForFirstNLayers | int | The number of first layers to disable the fan for. | Layers | Greater than or equal to 0.
enableFanTimeThreshold | int | If the print time of a layer is below this threshold (in seconds), the fan will be activated. | Seconds | Greater than or equal to 0.
slowDownTimeTreshold | int | If the print time of a layer is below this threshold (in seconds), the move speed will be slowed to attempt to get the layer print time up to this threshold. | Seconds | Greater than or equal to 0.
minPrintSpeed | int | The move speed will not be scaled down below this speed. | mm/s | Greater than 0.
customStartGCode | String | The custom G-Code to run when the material starts printing. | N/A | G-Codes that are understood by the printer.
customEndGCode | String | The custom G-Code to run when the material stops printing. | N/A | G-Codes that are understood by the printer.

## Slide 20: Material Configuration Object
Name | Data Type | Description | Units | Boundaries
extruderType | String | The type of extruder. | N/A | Within the set of available extruder types.
nozzleDiameter | double | The diameter of the nozzle in mm. | mm | Greater than or equal to 0.
xOffset | double | The x offset in respect to the position on the printer. | mm | Greater than or equal to 0.
yOffset | double | The y offset in respect to the position on the printer. | mm | Greater than or equal to 0.
zOffset | double | The z offset in respect to the position on the printer. | mm | Greater than or equal to 0.
customStartGCode | String | The custom G-Code to run when the extruder is activated for extrusion. | N/A | G-Codes that are understood by the printer.
customEndGCode | String | The custom G-Code to run when the extruder is deactivated after extrusion. | N/A | G-Codes that are understood by the printer.

## Slide 21: User Interface Layer

## Slide 22: Database Subsystem

## Slide 23: Persistence Framework Module
Interface | Information Required | Information Returned
getPrinterConfigurations | None | ArrayList<String> of names
getExtruderConfigurations | None | ArrayList<String> of names
getMaterialConfigurations | None | ArrayList<String> of names
getPrintJobConfigurations | None | ArrayList<String> of names
getPrintConfigurations | None | ArrayList<String> of names
getPrinterConfig | String name of the file | PrinterConfiguration Object
getExtruderConfig | String name of the file | ExtruderConfiguration Object
getMaterialConfig | String name of the file | MaterialConfiguration Object
getPrintJobConfiguration | String name of the file | PrintJobConfiguration Object
getPrintConfiguration | String name of the file | PrintConfiguration Object
savePrinterConfiguration | PrinterConfiguration Object | Boolean success state
saveExtruderConfiguration | ExtruderConfiguration Object | Boolean success state
saveMaterialConfiguration | MaterialConfiguration Object | Boolean success state
savePrintJobConfiguration | PrintJobConfiguration Object | Boolean success state
savePrintConfiguration | PrintConfiguration Object | Boolean success state
deletePrinterConfiguration | String name of the file | Boolean success state
deleteExtruderConfiguration | String name of the file | Boolean success state
deleteMaterialConfiguration | String name of the file | Boolean success state
deletePrintJobConfiguration | String name of the file | Boolean success state
deletePrintConfiguration | String name of the file | Boolean success state
Data | Source
PrinterConfiguration Object | Printer Hardware Configuration Controller
ExtruderConfiguration Object | Extruder Controller
MaterialConfiguration Object | Material Controller
PrintJobConfiguration Object | Print Job Controller
PrintConfiguration Object | Print Controller
Interfaces
Internal Data Descriptors

## Slide 24: Command Structure Module
Interfaces
Internal Data Descriptors
Data | Source
PrinterConfiguration Object | Persistence Framework
ExtruderConfiguration Object | Persistence Framework
MaterialConfiguration Object | Persistence Framework
PrintJobConfiguration Object | Persistence Framework
PrintConfiguration Object | Persistence Framework
External Data Descriptors
Data | Source
ArrayList<String> of file name | Storage Device (handled by OS)
XML files | Storage Device (handled by OS)
Interface | Information Required | Information Returned
getPrinterConfigurations | None | ArrayList<String> of names
getExtruderConfigurations | None | ArrayList<String> of names
getMaterialConfigurations | None | ArrayList<String> of names
getPrintJobConfigurations | None | ArrayList<String> of names
getPrintConfigurations | None | ArrayList<String> of names
getPrinterConfig | String name of the file | PrinterConfiguration Object
getExtruderConfig | String name of the file | ExtruderConfiguration Object
getMaterialConfig | String name of the file | MaterialConfiguration Object
getPrintJobConfiguration | String name of the file | PrintJobConfiguration Object
getPrintConfiguration | String name of the file | PrintConfiguration Object
savePrinterConfiguration | PrinterConfiguration Object | Boolean success state
saveExtruderConfiguration | ExtruderConfiguration Object | Boolean success state
saveMaterialConfiguration | MaterialConfiguration Object | Boolean success state
savePrintJobConfiguration | PrintJobConfiguration Object | Boolean success state
savePrintConfiguration | PrintConfiguration Object | Boolean success state
deletePrinterConfiguration | String name of the file | Boolean success state
deleteExtruderConfiguration | String name of the file | Boolean success state
deleteMaterialConfiguration | String name of the file | Boolean success state
deletePrintJobConfiguration | String name of the file | Boolean success state
deletePrintConfiguration | String name of the file | Boolean success state

## Slide 25: Requirements Traceability User Interface Layer
Number | Title | Interface Layer | Import GUI | Printer Configuration GUI | Material GUI | Print Configuration GUI | Print Job GUI | Status GUI | Extruder Configuration GUI | Import Controller | Printer Configuration Controller | Material Controller | Print Configuration Controller | Print Job Controller | Extruder Configuration Controller | Status Controller | Persistence Framework | Command Structure
3.1 | STL File Input | X | X |  |  |  |  |  |  | X |  |  |  |  |  |  |  | 
3.2 | Graphical User Interface (GUI) | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X
3.3 | Generate Machine Instructions |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.4 | Issue Machine Instructions |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.5 | Monitor Temperature | X |  |  |  |  |  | X |  |  |  |  |  |  |  | X |  | 
3.6 | Monitor Position |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.7 | Adhere to Material Constraints | X |  |  | X | X | X |  | X |  | X | X | X |  |  |  |  | 
3.8 | Identify Materials | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.9 | Identify Shapes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.1 | Determine Shape of Material Support Structure |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.11 | Create Printing Path |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.12 | Database Interface | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X
3.13 | Load & Store Materials | X |  |  | X |  |  |  |  |  |  | X |  |  |  |  | X | X
3.14 | Slice Geometry into Thickness Levels |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.15 | Monitor Flow Sensors |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3.17 | Allow for UV Head Polymerization | X |  |  | X |  |  |  |  |  |  | X |  |  |  |  |  | 
8.1 | Material Database | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X
8.2 | Abstract Hardware Interface | X |  | X |  |  | X |  |  |  | X |  |  | X |  |  |  | 
8.3 | Modular and Scalable Design | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X

## Slide 26: Requirements Traceability Processing Layers
Number | Title | Preprocessing Layer Object Subsection | Preprocessing Layer Object File Translation | Processing Layer Slicing Engine Wrapper | Post Processing Layer Parser | Post Processing Layer Unification
3.1 | STL File Input |  |  |  |  | 
3.2 | Graphical User Interface (GUI) |  |  |  |  | 
3.3 | Generate Machine Instructions |  |  | X | X | X
3.4 | Issue Machine Instructions |  |  |  |  | 
3.5 | Monitor Temperature |  |  |  |  | 
3.6 | Monitor Position |  |  |  |  | 
3.7 | Adhere to Material Constraints |  |  | X | X | X
3.8 | Identify Materials | X | X | X | X | X
3.9 | Identify Shapes |  |  | X |  | 
3.1 | Determine Shape of Material Support Structure |  |  | X |  | 
3.11 | Create Printing Path |  |  | X | X | X
3.12 | Database Interface |  |  |  |  | 
3.13 | Load & Store Materials |  |  |  |  | 
3.14 | Slice Geometry into Thickness Levels |  |  | X |  | 
3.15 | Monitor Flow Sensors |  |  |  |  | 
3.17 | Allow for UV Head Polymerization |  |  | X | X | X
8.1 | Material Database |  |  |  |  | 
8.2 | Abstract Hardware Interface |  |  |  |  | 
8.3 | Modular and Scalable Design | X | X | X | X | X

## Slide 27: Requirements Traceability Printer State, Communications and Printer Feedback Layers
Number | Title | Printer Control Layer Printer State Controller | Communications Serialization | Communications RxTx | Communications Deserialization | Printer | Printer Feedback Layer Dispatch
3.1 | STL File Input |  |  |  |  |  | 
3.2 | Graphical User Interface (GUI) |  |  |  |  |  | 
3.3 | Generate Machine Instructions | X |  |  |  |  | 
3.4 | Issue Machine Instructions |  | X | X | X |  | 
3.5 | Monitor Temperature | X | X | X | X | X | X
3.6 | Monitor Position | X | X | X | X | X | X
3.7 | Adhere to Material Constraints | X | X | X | X | X | X
3.8 | Identify Materials |  |  |  |  |  | 
3.9 | Identify Shapes |  |  |  |  |  | 
3.1 | Determine Shape of Material Support Structure |  |  |  |  |  | 
3.11 | Create Printing Path |  |  |  |  |  | 
3.12 | Database Interface |  |  |  |  |  | 
3.13 | Load & Store Materials |  |  |  |  |  | 
3.14 | Slice Geometry into Thickness Levels |  |  |  |  |  | 
3.15 | Monitor Flow Sensors | X |  | X | X | X | X
3.17 | Allow for UV Head Polymerization | X |  |  |  | X | 
8.1 | Material Database |  |  |  |  |  | 
8.2 | Abstract Hardware Interface | X |  |  |  | X | X
8.3 | Modular and Scalable Design | X | X | X | X | X | X

## Slide 28: Acceptance Plan
Package and Installation
  Thumb Drive Installation
Acceptance Criteria
  STL File Input
  Graphical User Interface
  Generate Machine Instructions
  Issue Machine Instructions
  Monitor Temperature
  Monitor Position
  Adhere to Material Constraints
  Identify Materials
  Identify Shapes
  Determine Shape of Material Support Structure
  Create Printing Path
  Database Interface
  Load and Store Materials
  Slice Geometry into Thickness Levels
  Monitor Flow Sensors
  Allow for UV Head Polymerization
  Material Database
  Abstract Hardware Interface
  Modular and Scalable Design